## Slide 1: TEKNOLOGI ENZIM
Pertemuan ke-5
Dr.oec.troph.Ir.Krishna Purnawan Candra, M.S.
Fakultas Pertanian Universitas Mulawarman

## Slide 2: Aktivitas Enzim
Kerja enzim / aktivitas enzim dinyatakan sebagai Unit (U), didefinisikan sebagai
  “Kerja enzim untuk menghasilkan produk sebanyak 1 mmol (mikromol) per menit”
Prinsip pengukuran/pengujian aktivitas enzim
  Mencampurkan enzim dlm suatu wadah bersama-sama dng substrat dan kofaktor dlm bentuk larutan yg mempunyai lingkungan ttu (pH dan salinitas)
  Menginkubasi campuran tersebut pada suhu dan waktu tertentu
  Menghentikan reaksi enzimatik dalam campuran tsb
  Mengukur jumlah produk yang dihasilkan

## Slide 3: Aktivitas Enzim
Pada prakteknya, kemudian aktivitas enzim ini kemudian dinyatakan sebagai U/mL
Ditemukan pada beberapa publikasi, satuan aktivitas enzim didefinisikan agak berbeda, yaitu dengan menyatakan jumlah produk yang berbeda (pmol, piko mol), atau langsung memasukkan unsur jumlah enzim (dalam mL)

## Slide 4: Aktivitas Enzim
Berkaitan dengan pemurnian enzim, dikenal istilah Aktivitas Spesifik, yaitu besarnya aktivitas enzim per jumlah protein yang terkandung dalam campuran enzim yang diuji
Makin besar suatu aktivitas spesifik enzim, maka makin besar tingkat kemurnian suatu enzim

## Slide 5: Uji aktivitas protease (Ketnawa et al., As J Food Ag-Ind 2(04): 457-468)
Determination of protease activity
The protease activity of bromelain was determined according to the casein digestion unit (CDU) method and tyrosine was used as a standard. The reaction mixture contained 0.1 mL enzyme solution, 0.8 mL of phosphate buffer pH 7.0 and 0.2 mL of 0.03M cysteine-0.006M EDTA. The mixture was incubated at 37°C for 10 min before starting the reaction by adding 1 mL of 1.5% casein solution. After exactly 5 min, the reaction was stopped by adding 3.0 mL 5% TCA. Precipitated protein was removed by centrifugation at 8000 rpm for 20 min. The absorbance of the clear supernatant was measured at 275 nm. One unit of protease activity is defined as the amount of enzyme releasing product equivalent to 1 μg of tyrosine min-1 mL-1 under the assay conditions.
Protein determination
Protein concentration of the sample was determined by using the Bradford method. The protein content was calculated by using BSA as a standard